## Slide 1
2. Spectral Vectors and Angles
Dr. David R. Thompson
Jet Propulsion Laboratory, Imaging Spectroscopy Group

## Slide 2
Goals for this module
Use basic mathematical tools including vector normalization and distance metrics
Use the spectral angle mapper to identify at least three of our target signatures

## Slide 3: Spectra are vectors
Channel 1
Channel 2
Spectra
Imagine each spectrum is a vector, e.g. a point in d-dimensional space, represented by d numbers each.
An image cube becomes a data cloud of points.
… now generalize this idea to 400 channels. We can’t visualize this, but the same mathematical tools apply.
a1, a2, … , ad]T

## Slide 4: Normalization
Vectors have direction and magnitude. Often we don’t care about the magnitudes of spectra, so we normalize them to some standard. To normalize a vector, we divide by the ”L2” (Euclidean)) norm defined as:
Other norms are possible. For example, the ”L1 norm” is the sum of elements.
All normalizations have the effect of equalizing the magnitudes of spectra to similar levels of brightness.

## Slide 5: The dot product operator
alternatively,
alternatively,
If is normalized, this is the magnitude of the orthogonal projection of onto :
It describes the similarity between and
For -dimensional column vectors and , their dot product is the scalar sum of element-wise products written:

## Slide 6: The Spectral Angle
It quantifies the match between spectral shapes, and is invariant to vector magnitudes.
The spectral angle is the arccosine of the normalized dot product. It describes the angle between two high-dimensional vectors.

## Slide 8: Exercise 2: Spectral angle mapping
N
100 m
Spectral angle for target 1
Full spectrum data cube
Target signatures (1 of 12)
Spectral Angle Calculation
Objective: Automate the scavenger hunt!
Calculate the spectral angle map for every signature.
Save a map for each answer. Does it match your intuition?