## Slide 1
9. Surface Reflectance
Dr. David R. Thompson
Jet Propulsion Laboratory, Imaging Spectroscopy Group

## Slide 2
Goals for this module
Understand the difference between linear and nonlinear mixing
Apply mixture models to synthesize mixed-pixel spectra
Unmix spectra with a spectral library

## Slide 3: Linear and Non-linear subspaces
Linear dimensionality reduction works best when spectra live (mostly) in a linear subspace.
Credit: wikimedia

## Slide 4: Linear vs. nonlinear mixtures of spectra
Credit: Keshava and Mustard, IEEE Signal Proc. Mag., 2002
Linear “geographic” or “areal” mixing is where spectra combine in in geographic proportion, a “checkerboard model” that is effective for many applications.
Nonlinear “intimate” mixing is a combination of scattering and reflection/absorption events. Minerals, tree canopies, urban environments, etc.

## Slide 5: Subpixel modeling: Gather a library of spectra
Could come from locations in the scene, prior observations, or field studies.
The panels at right show an example library formed of green vegetation (GV), soil, and nonphotosynthetic vegetation (NPV) spectra.

## Slide 6: Subpixel modeling
Geographic mixing (Linear model)
[Keshava and Mustard, IEEE 2002]
Library spectrum
Mixing fraction
r(λ) = Σi ai(λ) bi
Observed reflectance
We assume a geographic mixture model where all pixels are linear combinations of library spectra.
It is typical to force all bi to be nonnegative. “Sparsity” (i.e. lots of zero entries) may be favored.

## Slide 7: Multiple Endmember Spectral Mixture Analysis
A nonnegative least squares problem (all bi ≥ 0)
MESMA (Roberts et al., RSE 2003) finds the optimal compact combination of library endmembers to reproduce observations
Minimizes per-channel RMSE
Observed reflectance
in wavelength j
Library spectrum
Mixing fraction
Measurement noise

## Slide 8: Example of geographic mixing models
Chlorophyll
Liquid Water absorption
Water vapor absorption (remember?)
Surface reflectance in Visible ShortWave InfraRed (VSWIR), acquired by a Next Generation Imaging Spectrometer

## Slide 9: What surfaces are evident?
Dirt
Shade
Leaves

## Slide 10: Orchard example
shade
green
vegetation
soil
PCA Projection
The projection onto the first two principal components reveals a “simplex” of linear mixtures comprised of shade, soil, and vegetation.

## Slide 11: Continuum-absorption models
Another common model for reflectance spectra is to treat the reflectance as a linear or polynomial continuum, attenuated by one or more absorption features.
Continuum removal involves dividing by the linear continuum, transforming the absorption into a feature that is more invariant and insensitive to the substrate underneath.
Here, the library holds the absorption signatures. A fitting algorithm matches them to the continuum-removed spectra.
The panel at right shows a Hematite absorption feature from the USGS spectral library. The continuum appears in grey.

## Slide 12: Placing the continuum is an art!
?
Absorptions
Continuum

## Slide 13: Inversion options
Standard least squares minimization:
Nonnegative least squares (Lawson/Hansen algorithm, iterative):
A library matrix where columns are spectra
Vector of mixing coefficients
Measured spectrum
minimizes
minimizes

## Slide 15: Exercise 9: Spectral unmixing
Objective: Unmix the list of spectra in the citrus orchard overflight.
Plot the model fits and nonzero component spectra for some representative examples. The right panel shows spectrum #1000.
Extra credit: interpret your endmembers, and find the mixture fractions of vegetation, nonphotosynthetic vegetation, soil and shade.