## Slide 1
10. Noise, Distortions, and the MNF Transform
Dr. David R. Thompson
Jet Propulsion Laboratory, Imaging Spectroscopy Group
July 20, 2019

## Slide 2
Goals for this module
Recognize different flavors of instrument noise and systematics
Estimate instrument noise from imaging spectroscopy data
Calculate the Minimum Noise Fraction (MNF) transformation

## Slide 3: Physical instruments produce various flavors of distortion:
Grating
Slit
Focal Plane
Array
Telescope
Photon shot noise: magnitude is square root of signal due to Poisson counting statistics
Electronic read noise: magnitude is usually independent of signal
Nonlinearities: departure of radiometric response from idealized proportional description
Other Systematics: Optical ghosting, electronic panel effects, calibration error, etc.
Highly instrument-specific.
Our emphasis

## Slide 4: Example of systematic electronic effects
In-flight estimates for the PRISM instrument
Permits updated synthetic flat field and per-element instrument noise estimation
[Thompson et al., Remote Sensing of Environment 231, 2019]

## Slide 5: Noise has a covariance structure!
[From Thompson et al., RSE 2019]

## Slide 6: First-principles noise estimation
Grating
Slit
Focal Plane
Array
Telescope
Radiometric uncertainty by forward propagation of photon counting and electronic noise statistics
Fit models by analysis and/or laboratory characterization
SNR is signal-dependent in shot noise-limited systems
Pro: SI-traceability; component-wise models; high accuracy
Con: In-flight validation & updates difficult, pathological illumination, tricky to get covariance structure

## Slide 7: Scene-based noise estimation
Estimate radiometric uncertainty directly via empirical statistics
Can exploit scene homogeneity assumptions or reflectance basemaps
Easier than vicarious characterization, but not suitable for all scenes
Von Neuman’s approximation based on pairwise differences:
Applied separately in each channel, preferably along pushbroom (down-track) dimension to characterize each element independently.
[Von Neumann, J. Ann. Math. Statist. 12 367–395. (1941). MR0006656]

## Slide 8: Scene-based noise estimation (contd.)
Nonparametric smoothing alternative – subtract the “scene contribution”. If the scene is smooth, the scene part can be approximated by smoothing (i.e. convolve a Gaussian):
Recall our empirical expression for the sample covariance matrix:
Original Image
Subset (550 nm)
Scene, smoothed in the downtrack dimension
“Noise contribution”
is the remainder
[Thompson et al., Optics Express 2017]
Total = Scene + Noise

## Slide 9: The MNF transformation: two linear rotations
As detailed in: A. A. Green, et al, IEEE Trans. Geosci. Remote Sens., vol. 26, no. 1, pp. 65–74, Jan. 1988.
Make the signal zero mean (subtract µ from each spectrum)
Calculate the eigenvalues and eigenvectors of the noise covariance, perhaps with SVD
“Whiten” the noise to remove influence of noise covariance
Apply Principal Component Analysis
Result: PCA, but scaled so that noise level is unity
Noise-whitened data matrix
Diagonal matrix, reciprocal of square root of N’s eigenvalues
Eigenvectors of noise covariance N
Zero-meaned data matrix
Eigenvectors of noise-whitened covariance matrix
Data in MNF projection

## Slide 10: Typical SNR curves
From Mouroulis et al., OE 2016
Question: how can SNR be so high when the radiance level is so low?

## Slide 11: Tuned grating efficiencies
From Mouroulis et al., OE 2016

## Slide 12: Potential error sources
Raw Digital Numbers
Radiance at sensor
Surface Reflectance
Geophysical Map
Quantization error (bit rate)
(Influenced by observation noise)
Atmospheric unknowns (aerosol types, gas and particle vertical profiles)
Bi-directional reflectance
Topographic effects
Temporal variability
Retrieval models
Generalizing local parameterizations
Diverse in-situ data sources
Detector sensitivity drift
Transient or systematic electronic effects
Long term degradation and contamination
Spectral response uncertainty

## Slide 13: Climatological uncertainties: AOD550
ENF
EBF
DF
DBF
MF
CS
OS
WS
S
G
PW
C
U
CM
B
Land cover classification
MODIS average AOD550
[Thompson et al., Remote Sensing of Environment 232, 2019]

## Slide 14: Climatological uncertainties: water vapor
ENF
DF
DBF
MF
CS
OS
WS
S
G
PW
C
U
CM
B
EBF
MODIS average water vapor gm cm-2
Land cover classification
[Thompson et al., Remote Sensing of Environment 232, 2019]

## Slide 15: Atmospheric correction artifacts
From Clark et al., 2002.

## Slide 16: Atmospheric aerosol-related artifacts
Path radiance
Reduced contrast
H2O vapor residuals
Note: different optical types have different effects on the spectrum. Some tend to absorb strongly (e.g. soot) while others are “scattering” (e.g. some dust). Their signatures may have different shapes depending on the specific particle shape, composition, and size.