## Slide 1
11. Optimal Estimation: Theory and Practice
Dr. David R. Thompson
Jet Propulsion Laboratory, Imaging Spectroscopy Group
July 20, 2019

## Slide 2
Goals for this module
Apply Optimal Estimation to fit combined surface and atmosphere models
Construct new prior distributions
Correctly balance instrument and prior information

## Slide 3: Global spectroscopy missions are an atmospheric correction challenge
Sequential methods face difficulties in certain observing conditions:
High water vapor
Extreme viewing angles
Surface/atmosphere coupling
Heavy aerosol loads
Orbital missions access tropical and subtropical environments that:
Host a large fraction of Earth’s productivity and biodiversity
Are underrepresented in atmospheric correction research
Often have “difficult” atmospheres
Most aerosol retrieval methods use dark or shadowed pixels that may not be apparent at orbital ground sampling resolutions
Existing methods generally disregard uncertainties, which are important to generalize existing regional studies to bias-free global maps

## Slide 4: Optimal Estimation Theory: Simultaneous estimation of surface and atmosphere
A true spectroscopic retrieval that can exploit information distributed across the spectrum, helping to disentangle surface and atmosphere
A rigorous probabilistic formulation incorporates ancillary measurements via the prior distribution
Comprehensive uncertainty estimates can inform downstream analyses and global maps
Flexible state vectors, more robust for difficult observing conditions
Elegant, conceptually simple
Popularized for remote sensing by C. C. D. Rogers, e.g. his 2000 book
Notes: Traditional atmospheric correction typically: (!) LUT generation of coefficients, (2) estimate of atmospheric state, (3) algebraic correction based on lambertian assumptions. Mature and effective; form basis of methods used in AVIRIS-NG standard products.
Several challenges to this…
limited size of state vector
Algebraic approximate solutions less accurate for extreme geometries
Uncoupled
Algebraic inversion means difficult to tease apart smooth atmospheric effects
Most inaccurate in regions of high haze, extreme water vapor causing absorption in scattering. India dataset contains pushes the frontier, excelelnt opportunity for investigating next level of precision.
Enabled by a fast radiative transfer model as an interior loop of an iterative max. a posteriori estimation

## Slide 5: The “forward problem”
5
State vector
Measurement
Forward model

## Slide 6: The “inverse problem”
6
Estimated state vector
Measurement
Inversion algorithm

## Slide 7: Maximum A Posteriori solution
Taking the logarithm of , and ignoring terms that are constant with , reduces the Maximum A Posteriori problem to the optimization:
… we can solve it by conjugate gradient descent.
Bayesian prior
Model match to measurement
Cost

## Slide 8: “Classic” atmospheric correction: a sequential operation
Lookup table indexed by H2O, etc.
1. In advance, do RTM calculations for a grid of atmospheric conditions:
TOA reflectance
Surface reflectance
4. Algebraic Inversion
2. Analyze radiance to estimate this atmosphere (typically using band ratios).
Path reflectance of atmosphere
Spherical sky albedo
Upward/downward transmission along optical path for known geometry
3. Look up and/or interpolate optical coefficients
Notes: With atmospheric state specified, We can get optical constants via linear lookup table interpolation (note: T=transmission, S=spherical sky albedo, rho_a is the path reflectance).
This is just one of several similar functional approximations to the actual radiative transfer solution. With atmosphere specified, we can invert it algebraically to recover the surface reflectance.
The conventional strategy is limited in sever

## Slide 9: OE: Iterative simultaneous estimation of atmosphere and surface
Bayesian prior
Model match to measurement
Cost
1. Predict radiance
2. Optimize state vector

## Slide 10: The Jacobian: The state’s influence on an observable
Consider the first order Taylor series expansion:
A local approximation, which is exact for linear problems
Elements of :

## Slide 11: The Jacobian: The state’s influence on an observable
A more compact form:
Written explicitly as:
where

## Slide 12: The Jacobian: The state’s influence on an observable
A single reflectance value
Atmospheric H2O column

## Slide 13: Posterior predictive uncertainty
xATMOS
xSURFACE

## Slide 14: Variability due to measurement noise vs. unknown state parameters
Total observation noise
Measurement noise (instrument effects)
Photon noise
Read noise
Dark current noise
Unknown parameters in the observation system
Sky view factor
H2O absorption coefficient intensity
Systematic radiative transfer error
Uncorrelated radiative transfer error
Jacobian WRT unknowns

## Slide 15: Case study [Thompson et al., Remote Sensing of Environment 218, 2018]
I
N
1000 m
V
VI
N
100 m
IV
II
III
N
100 m
In-situ AOD via Reagan sunphotometers
In-situ surface reflectance via ASD Fieldspec
Ivanpah Playa
California Institute of Technology
Jet Propulsion Laboratory
Notes: We measured 6 sites at Ivanpah, JPL, and Caltech.

## Slide 16: Model components
Pre-defined
Statistical, fit to data
Retrieved in the inversion
Instrument: AVIRIS-NG
Instrument model with Wavelength- and signal-dependent SNR
Photon shot & read noise
Uncorrelated calibration uncertainty
Systematic calibration / RT uncertainty
Atmosphere: MODTRAN 6.0 RTM
DISORT MS, Correlated-k
Rural aerosol model
broad prior uncertainties
Unmodeled unknowns, including H2O absorption coefficients
H2O, AOD retrieved
Surface: Multi-component Multivariate Gaussians
Prior based on universal library, highly regularized to permit accurate retrieval of arbitrary shapes
Reflectance estimated independently in every channel

## Slide 17: Example of multi-component surface models
[Thompson et al., Remote Sensing of Environment 216, 2018]

## Slide 18: Reflectance estimate vs. in situ [Thompson et al., Remote Sensing of Environment 2018]
Wavelength (nm)
Wavelength (nm)
Notes: Good agreement!

## Slide 19: Aerosol fitting results [Thompson et al., Remote Sensing of Environment, 232, 2019].
Aerosol distortion
Aerosol-related H2O vapor distortions
H2O vapor distortions
Original method
New approach
Simultaneous estimation of surface and atmosphere parameters can account for aerosol distortions
We retrieve three optical types (best interpreted as structured error terms rather than physical particle properties)
Validation on a large segment of the AVIRIS-NG campaign in India, which experienced high water vapor and AOD loadings
AOD550 estimates for AVIRIS-NG India campaign
Original
OE solution
Aerosol type
fractions
Aerosol type
fractions

## Slide 20: Modeling assumptions affect the relative weighting of measurement and prior
Wavelength (nm)
[Thompson et al., Remote Sensing of Environment 216, 2018]

## Slide 21: Coastal environments [Thompson et al., Remote Sensing of Environment 231, 2019]
Notes: Posterior uncertainty predictions (grey envelopes) accurately predict and capture our actual discrepancies!
This demonstrates a closed account of the uncertainty in the system. To our knowledge, this is the first time it has been done for VSWIR imaging spectroscopy.
Note: we also account for the uncertainty in the surface measurement, which is a significant contributor to the confidence bands.

## Slide 22: Example: volcano AOD observations
AVIRIS-C f170127t01p00r16
(subset, visible bands)
Aerosol Optical Depth at 550 nm
Aerosol Optical Depth Uncertainty
Hot crater
[Realmuto, Thompson, et al., in preparation]
Combined estimate of H2O vapor, AOT, surface reflectance and temperature